## Slide 1: Coordinated Movement
Individuals can
1. make decisions that compliment each other
2. can make a decision as a whole and move in a prescribed, coordinated group
Formation: a set of locations where a character can be positioned. One location is the leader position.
Formation motion is the movement of a group of characters retaining group organisation (under 2.)

## Slide 2: Formation Movement
Movement of NPCs so that they retain some group arrangement.
  For Example, Fixed Geometric Patterns
      Single file, row, V-shape,
  Used in
    Team Sports, Squad Based games, RTS
  and also in
    FPS, Driving, Action Adventure
Both Simple and Flexible
  more stable and easier to write than collaborative tactical decision making

## Slide 3: Fixed Formations
Defined as a set of position slots
  locations where a character can be positioned
    relative to leader
Leader slot defines origin for position and orientation
Leader moves as normal
Pattern is translated and oriented so that the leader is in the leader slot and facing appropriate direction
Notes: Line
V or “finger four”
Defensive circle
Two abreast in cover

## Slide 4: Fixed Formations
As leader moves so pattern moves
Each character fits into a slot
Can be assigned directly
  i.e. match position and orientation without needing kinematic or dynamic steering behavior
Examples:
  Line, Circle, Two abreast in cover, V or “Finger Four”

## Slide 5: Calculating Position
If slot is at position rs relative to the leader slot then position of NPC at that slot is:
ps = pl + (Ωl * rs)
pl = position of leader
Ωl = orientation of leader (in matrix form)
Orientation of NPC in slot is:
Os = wl + ws
Wl = orientation of the leader
Ws = orientation of slot s, relative to the leader
Or in SFML just use an SF::Trasform
Notes: orientation in matrix form otherwise know as a rotation matrix (checkout: https://en.wikipedia.org/wiki/Rotation_matrix)

## Slide 6: Leader Movement
Movement of NPC should take into account the fact that it is leader
  Limits on speed it can turn
Collision detection should take into account the size of the formation
Difficult to use in complex formations

## Slide 7: Example - Overlord
Player controls the minions
Minions move in pyramid formation

## Slide 8: Example
Squad Movement Formations & Techniques
https://www.youtube.com/watch?v=OKRues4Fwrk
Game of Thrones
https://www.youtube.com/watch?v=dmP35y8xXxU

## Slide 9: Scalable Formations?
Scale depending on number of NPCs
Slots are dynamic
  No explicit list of slot locations
  e.g. defensive circles
Algorithm can be much more complex

## Slide 10: Emergent Formations
Another approach to scalability
Each individual NPC uses a steering behavior
Chooses another slot in the formation
  (e.g. nearest one)
Uses this as target (if not already being used)
If target is unobtainable
  e.g. is in wall or obstacle
  choose another slot
Works much like flocking
  But formation emerges from individual rules

## Slide 11: Emergent Formations
Or specify a general rule e.g. v-formation
Simple and effective
Each NPC can react individually
  to obstacles and potential collisions
  No need to worry about formation size
But can be difficult to get rules just right
Debugging emergent formations can be difficult
  of little use for military groups because of characteristic disorder